Ethernet to MERG-CBUS interface	Revised	: April 24, 2012
CAN-GC1E	Revision	: 1.1
Bill Of Materials	Revisor	: Peter Giling
************************************************************
Qty Reference	Part

1	R1	470 Ohm
2	R2,R7	120 Ohm
3	R3,R4,R5	220 Ohm
1	R6	47 KOhm
1	R8	100 KOhm
3	R9,R19,R20	10 KOhm
1	R10	2,32 KOhm 1% metalfilm
2	R11,R17	270 Ohm
4	R12,R14,R15,R16	49,9 Ohm 1% metalfilm
1	R18	2,2 KOhm 1% metalfilm
1	C1	ELCO RAD 4.700/35 rad
2	C2,C4	RAD 100/35 rad
1	C3	RAD 1.000/25V rad
2	C5,C13	Elco 10 uF 16V rad
5	C6,C7,C8,C16,C17	100 nF
1	C9	220 nF
2	C14,C15	15 pF
1	C18	Elco 1000 uF/16V rad
1	D1	1N5822
1 D2	1N5818
1	LED1	LED Yellow
1	LED2	LED Green
2	LED3,LED5	LED B-3 GN
1	LED4	LED B-3-RT
1	U1	PIC18F2585 With socket Dil28s
1	U2	ENC28J60 With socket Dil28s
1	U3	MCP2551 With socket Dil08
1	VR1	LM2576-12
1	VR2	LM2575T-5
1	VR3	LF33CV
2	JP1, JP2	JUMPER
1	ICSP1	6 pin header (or Farnell 167-5768)
1	J1	AKL220/02 + AKL249/02 ( Reichelt )
2	J2,J3	D-SUB BU 09EU
1	J4	Magjack ethernet connector
1	J5	AKL230-04 + AKL249-04 ( Reichelt )
1	Pot1	Trimmer 1 Kohm
1	PB1	BUTTON (Reichelt 3301B)
1	L1	Inductor 100 uH ( Reichelt FED 100)
2	L2,L3	Inductor 330uH (Reichelt 09P 330)
1	Res1	Resonator 8 MHz
1	X1	Crystal 25 MHz
1	F1	PFRA 185 1,8Amp autofuse
1	GR1	KBU6B Bridge rectifier 6 Amp
1	Cooling	V PR127/94-M3
3	Clips TO-220	MC 725
4	Supports M4 x 10
4	Screws M4 x 8

Important !!!!!!
For Power IC and Regulators:
First mount cooling device with screws, then insert IC and regulators, bending wires so that they are flat to cooling, then fix clamps to hold IC's and after that solder IC's.