Giling Computer Applications

CAN-BUS servo decoder	Revised: March 4, 2012
CAN-GC6	Revision: 2.3
Bill Of Materials

Qty Ref	Part

 4 R1..R4	470 Ohm
 9 R6,R8.R12,R14,R15,R32	10 KOhm
 1 R7	47 KOhm
 4 R16..R19	270 Ohm
 4 R20..R23	1,5 KOhm
 8 R24..R31	1 KOhm
 1 R33	100 KOhm
 1 R34	120 Ohm
 3 C1,C2,C5	ELCO SM 10uF 16Vrad
 2 C3,C4	100 nF
 3 D1,D2,D3	DIODE 1N4002
 2 L1,L4	Reichelt LED B-3 RT
 1 L2	LED 3mm green
 1 L3	LED 3mm yellow
 2 VR1,VR2	7805 TO220
 1 U1	PIC18F2480 with socket DIL28s
 1 U2	MCP2551 with socket DIL8
 2 U4,U5 (****)	LTV844 or 2 x LTV824
 1 ICSP1	Farnell 167-5768
 1 GCA137 (*)	Female header 3 pins (2.54 mm)
 1 PB1	Reichelt taster 3301B
 1 Res1	RESONATOR 8MHz
 1 JP1	2 pin header with jumper
 1 J1 (**)	Reichelt D-SUB BU 09EU
 1 J2 (**)	Reichelt D-SUB ST 09EU
 1 J3 (***)	Reichelt AKL230-04 + AKL249094
 4 S1..S4	Reichelt PSS254/03
 4 F1..F4 (****)	Reichelt PSS254/03
 4 support	M4
 4 screws	M4
 1 Pc-board	CAN-GC6 V2.3
 1 connector cpl	Sub-D-9 male with housing
 1 connector cpl	Sub-D-9 female with housing

Remark:

(*)	Only to be installed if GCA137 is used on top
(**)	Only to be installed if GC6 is used in CAN-GC system
(***)	Only to be installed if GC6 is used in MERG Cbus system
(****)	Only to be installed if limit switches will be connected.